## Slide 1: Programming Project Discussion
QR Decoder
Before you get started: you must download and run TCPEchoClient.c and TCPEchoServer.c

## Slide 2: Infrastructure
You may either use the class VMs available at secnet.cs.wpi.edu/vmdashboard or
Set up your own isolated network using Vbox, Parallel (may look up online tutorials that can help with the set up)

## Slide 3: Getting started
For a basic functionality, you need to be able to read and transmit a binary file.
From the project specs, you are given a URL where you can generate your own QR codes and save those as image files that can be later used for the transmission.
The client code needs to get the file name of the png file. It will read each of the bytes (image is nothing but bytes/bits) into a buffer and it will then send system call on that buffer and you will read this in a while loop – reading x number of bytes and send x number of bytes and continue until the end of the file (image file). *

## Slide 4: *How to figure out the size of the image?
Required because you need to send the size of the file first.
  There are a few different techniques to achieve this. One way would be to use a system call that helps us get stats associated with a file. Can you figure which one is that? That will help you get the size of the file in bytes.
  Another way might be to seek into a file (lookup lseek) until the end of the file without reading any bytes along the way and ftell to tell how far you are. Once you figured that out, you can go back to the beginning of the file to actually start reading (see below)
  - for reading cmd arguments, getopt()
  - setsockopt(so_reuseaddr)
  - reading and transmitting a binary file
  -- fopen (,"rb") and "wb"
  - how big the transmitted file is
  -- fseek, ftell, rewind => find length from here and use it below

## Slide 5: Server’s responsibilities
Start reading: https://man7.org/linux/man-pages/man2/recv.2.html
Some pseudocode:
  u_int32_t length;
  recv (sock, &length, 4, 0); //to receive the length
  char buffer[10000]; //is this a pointer? Also, char is one byte
  u_int32_t bytesReceivedsoFar = 0
  while (bytesReceivedsoFar < length) {
  bytesActuallyReceived = recv(sock, buffer+bytesReceived, length-bytesReceived, 0)
  bytesReceivedsoFar += bytesActuallyReceived
  }
  //write the buffer

## Slide 6: Client’s Responsibilities
Send (sock, buffer, 10000, 0)
You can hardcode information about the server (IP and port #)

## Slide 7: Writing an image to a file
Steps involved:
Open file (.png name)
Write buffer to a file
Close file

## Slide 8: Parsing command line arguments
A good reference would be https://www.gnu.org/software/libc/manual/html_node/Getopt-Long-Option-Example.html (you may lookup more examples for this function getopt_long and getopt_long_only)
(from the project specs), you should also assign default values to anything that is missing in the arguments

## Slide 9: Configuring Host
This is where you will include your typical code to configure the host and connect to a port (see below the code taken from Beej’s guide.). Please understand the code before adopting it.
memset(&hints, 0, sizeof hints);
hints.ai_family = AF_UNSPEC;
hints.ai_socktype = SOCK_STREAM;
if ((rv = getaddrinfo(NULL, PORT, &hints, &servinfo)) != 0) {
fprintf(stderr, "getaddrinfo: %s\n", gai_strerror(rv));
return 1;

## Slide 10: Creating Sockets
Next, you need to use socket() and setsockopt() to create sockets. You may use the following code from Beej's guideLinks to an external site. to help you.
socket(p->ai_family, p->ai_socktype, p->ai_protocol)) == -1)
{
perror("server: socket");
}
if (setsockopt(sockfd, SOL_SOCKET, SO_REUSEADDR, &yes,
sizeof(int)) == -1) {
perror("setsockopt");
exit(1);
}

## Slide 11
4. Binding to Socket
5. Listening on a Socket
(the above two should be very familiar by now. Additionally, you may continue to refer to Beej's guide: https://beej.us/guide/bgnet/examples/server.c. for the implementation of bind and listen)
6. Handling Client Connections
-> this is where you will keep track of client requests, maximum connections and client rate. We must allow for an endless loop to handle/monitor connections, first. You may do a web search for "handling multiple client connections in C server" for some sample code. (don't forget to cite the source should you adopt anyone else's code). One example can be found here: https://www.gnu.org/software/libc/manual/html_node/Server-Example.html
Your server code must constantly look for activity from client. This could be done with the help of select() (see the server example on the URL above). And as discussed in the server example on GNU's website, you may look to service all the sockets with pending input using FD_ISSET and accept().
If there is a new client, getnameinfo() can help get the numeric hostname and service name, for a given socket address.
Next, you must store the newly added client's information and note the time in seconds for the connection start. You must log this information in your log file (see #7 below).
You must constantly check for the maximum number of connections allowed (3 in our case). If max (=3) is reached, you may not allow any more connections by simply disconnecting a client (you may use a combination of send() and close() to communicate with this fourth client).
Now you have clients in the system, you need to handle their requests.

## Slide 12
7. Logging Activity
-> This will be a simple function that will log time and client IP in a particular format (something similar to https://stackoverflow.com/questions/23856306/how-to-create-log-file-in-c ). To log time, you will need your localtime so you may follow the sample code discussed here https://stackoverflow.com/questions/7411301/how-to-introduce-date-and-time-in-log-file

## Slide 14: Elementary TCP Sockets
Contents from
UNIX Network Programming
Vol. 1, Second Ed. Stevens
Chapter 4
Optional Reading
http://beej.us/guide/bgnet/

## Slide 15: TCP Sockets Outline
Socket Address Structure
TCP and UDP call Sequences
Socket
Connect
Bind
Listen
Accept
Close
Example: TCP Echo Server and Client [old]

## Slide 16: IPv4 Socket Address Structure
The Internet socket address structure is named sockaddr_in
and is defined by including <netinet/in.h> header.
struct in_addr {
in_addr_t s_addr /* 32-bit IP address */
}; /* network byte ordered */
struct sockaddr_in {
uint8_t sin_len; /* length of structure (16) */
sa_family_t sin_family; /* AF_INET */
in_port_t sin_port; /* 16-bit TCP or UDP port number */
/* network byte ordered */
struct in_addr sin_addr; /* 32-bit IPv4 address */
/* network byte ordered */
char sin_zero[8]; /* unused */
};

## Slide 17: The Socket Interface
Application 1
Socket
socket interface
user
kernel
Application 2
user
kernel
Underlying communication Protocols
Underlying communication Protocols
Communications network
Socket
socket interface

## Slide 18: TCP Socket Calls
socket()
bind()
listen()
read()
close()
socket()
connect()
read()
write()
close()
blocks until server receives
a connect request from client
data
data
Server
Client
accept()
write()
connect negotiation

## Slide 19: UDP Socket Calls
socket()
bind()
sendto()
close()
socket()
bind()
recvfrom()
sendto()
close()
blocks until server
receives data from client
data
data
Server
Client
recvfrom()
Not needed

## Slide 20: System Calls for Elementary TCP Sockets
#include <sys/types.h>
#include <sys/socket.h>
family: specifies the protocol family {AF_INET for TCP/IP}
type: indicates communications semantics
SOCK_STREAM stream socket TCP
SOCK_DGRAM datagram socket UDP
SOCK_RAW raw socket
protocol: set to IPPROTO_TCP for TCP
returns on success: socket descriptor {a small nonnegative integer}
on error: -1
Example:
if (( sd = socket (AF_INET, SOCK_STREAM, IPPROTO_TCP)) < 0) err_sys (“socket call error”);
socket Function
int socket ( int family, int type, int protocol );

## Slide 21: Connect Function
sockfd: a socket descriptor returned by the socket function
*servaddr: a pointer to a socket address structure
addrlen: the size of the socket address structure
The socket address structure must contain the IP address and the port number for the connection wanted.
In TCP connect initiates a three-way handshake. connect returns only when the connection is established or when an error occurs.
returns on success: 0
on error: -1
Example:
if ( connect (sd, (struct sockaddr *) &servaddr, sizeof (servaddr)) != 0)
err_sys(“connect call error”);
int connect (int sockfd, const struct sockaddr *servaddr,
socklen_t addrlen);

## Slide 22: TCP Socket Calls
socket()
bind()
listen()
read()
close()
socket()
connect()
read()
write()
close()
blocks until server receives
a connect request from client
data
data
Server
Client
accept()
write()
connect negotiation

## Slide 23: Bind Function
int bind (int sockfd, const struct sockaddr *myaddr, socklen_t addrlen);
bind assigns a local protocol address to a socket.
protocol address: a 32 bit IPv4 address and a 16 bit TCP or UDP port number.
sockfd: a socket descriptor returned by the socket function.
*myaddr: a pointer to a protocol-specific address.
addrlen: the size of the socket address structure.
Servers bind their “well-known port” when they start.
returns on success: 0
on error: -1
Example:
if (bind (sd, (struct sockaddr *) &servaddr, sizeof (servaddr)) != 0)
errsys (“bind call error”);

## Slide 24: Listen Function
int listen (int sockfd, int backlog);
listen is called only by a TCP server and performs two actions:
1. Converts an unconnected socket (sockfd) into a passive socket.
2. Specifies the maximum number of connections (backlog) that the kernel should queue for this socket.
listen is normally called before the accept function.
returns on success: 0
on error: -1
Example:
if (listen (sd, 2) != 0) errsys (“listen call error”);

## Slide 25: Accept Function
int accept (int sockfd, struct sockaddr *cliaddr, socklen_t *addrlen);
accept is called by the TCP server to return the next completed connection from the front of the completed connection queue.
sockfd: This is the same socket descriptor as in listen call.
*cliaddr: used to return the protocol address of the connected peer process (i.e., the client process).
*addrlen: {this is a value-result argument}
before the accept call: We set the integer value pointed to by *addrlen to the size of the socket address structure pointed to by *cliaddr.
on return from the accept call: This integer value contains the actual number of bytes stored in the socket address structure.
returns on success: a new socket descriptor
on error: -1

## Slide 26: Accept Function
For accept the first argument sockfd is the listening socket
and the returned value is the connected socket.
The server will have one connected socket for each client connection accepted.
When the server is finished with a client, the connected socket must be closed.
Example:
sfd = accept (sd, NULL, NULL);
if (sfd == -1) err_sys (“accept error”);
connected socket
int accept (int sockfd, struct sockaddr *cliaddr, socklen_t *addrlen);

## Slide 27: Close Function
int close (int sockfd );
close marks the socket as closed and returns to the process immediately.
sockfd: This socket descriptor is no longer useable.
Note – TCP will try to send any data already queued to the other end before the normal connection termination sequence.
returns on success: 0
on error: -1
Example:
close (sfd);

## Slide 28: TCP Echo Server
#include <stdio.h> /* for printf() and fprintf() */
#include <sys/socket.h> /* for socket(), bind(), and connect() */
#include <arpa/inet.h> /* for sockaddr_in and inet_ntoa() */
#include <stdlib.h> /* for atoi() and exit() */
#include <string.h> /* for memset() */
#include <unistd.h> /* for close() */
#define MAXPENDING 5 /* Maximum outstanding connection requests */
void DieWithError(char *errorMessage); /* Error handling function */
void HandleTCPClient(int clntSocket); /* TCP client handling function */
D&C

## Slide 29: TCP Echo Server (cont)
int main(int argc, char *argv[])
{ int servSock; /*Socket descriptor for server */
int clntSock; /* Socket descriptor for client */
struct sockaddr_in echoServAddr; /* Local address */
struct sockaddr_in echoClntAddr; /* Client address */
unsigned short echoServPort; /* Server port */
unsigned int clntLen; /* Length of client address data structure */
if (argc != 2) /* Test for correct number of arguments */
{
fprintf(stderr, "Usage: %s <Server Port>\n", argv[0]);
exit(1);
}
echoServPort = atoi(argv[1]); /* First arg: local port */
/* Create socket for incoming connections */
if ((servSock = socket (AF_INET, SOCK_STREAM, IPPROTO_TCP)) < 0)
DieWithError("socket() failed");
D&C

## Slide 30: TCP Echo Server (cont)
/* Construct local address structure */
memset(&echoServAddr, 0, sizeof(echoServAddr)); /* Zero out structure */
echoServAddr.sin_family = AF_INET; /* Internet address family */
echoServAddr.sin_addr.s_addr = htonl(INADDR_ANY); /* Any incoming interface */
echoServAddr.sin_port = htons(echoServPort); /* Local port */
/* Bind to the local address */
if (bind (servSock, (struct sockaddr *) &echoServAddr, sizeof(echoServAddr)) < 0)
DieWithError("bind() failed");
/* Mark the socket so it will listen for incoming connections */
if (listen (servSock, MAXPENDING) < 0)
DieWithError("listen() failed");
D&C

## Slide 31: TCP Echo Server (cont)
for (;;) /* Run forever */
{
/* Set the size of the in-out parameter */
clntLen = sizeof(echoClntAddr); /* Wait for a client to connect */
if ((clntSock = accept (servSock, (struct sockaddr *) &echoClntAddr, &clntLen))
< 0) DieWithError("accept() failed");
/* clntSock is connected to a client! */
printf("Handling client %s\n", inet_ntoa(echoClntAddr.sin_addr));
HandleTCPClient(clntSock);
}
/* NOT REACHED */
}
D&C

## Slide 32: TCP Echo Client
#include <stdio.h> /* for printf() and fprintf() */
#include <sys/socket.h> /* for socket(), connect(), send(), and recv() */
#include <arpa/inet.h> /* for sockaddr_in and inet_addr() */
#include <stdlib.h> /* for atoi() and exit() */
#include <string.h> /* for memset() */
#include <unistd.h> /* for close() */
#define RCVBUFSIZE 32 /* Size of receive buffer */
void DieWithError(char *errorMessage); /* Error handling function */
D&C

## Slide 33: TCP Echo Client (cont)
int main(int argc, char *argv[])
{
int sock; /* Socket descriptor */
struct sockaddr_in echoServAddr; /* Echo server address */
unsigned short echoServPort; /* Echo server port */
char *servIP; /* Server IP address (dotted quad) */
char *echoString; /* String to send to echo server */
char echoBuffer[RCVBUFSIZE]; /* Buffer for echo string */
unsigned int echoStringLen; /* Length of string to echo */
int bytesRcvd, totalBytesRcvd; /* Bytes read in single recv() and total bytes read */
if ((argc < 3) || (argc > 4)) /* Test for correct number of arguments */
{
fprintf(stderr, "Usage: %s <Server IP> <Echo Word> [<Echo Port>]\n",
argv[0]);
exit(1)
}
D&C

## Slide 34: TCP Echo Client (cont)
servIP = argv[1]; /* First arg: server IP address (dotted quad) */
echoString = argv[2]; /* Second arg: string to echo */
if (argc == 4)
echoServPort = atoi(argv[3]); /* Use given port, if any */
else
echoServPort = 7; /* 7 is the well-known port for the echo service */
/* Create a reliable, stream socket using TCP */
if ((sock = socket (AF_INET, SOCK_STREAM, IPPROTO_TCP)) < 0)
DieWithError("socket() failed");
/* Construct the server address structure */
memset(&echoServAddr, 0, sizeof(echoServAddr)); /* Zero out structure */
echoServAddr.sin_family = AF_INET; /* Internet address family */
echoServAddr.sin_addr.s_addr = inet_addr(servIP); /* Server IP address */
echoServAddr.sin_port = htons(echoServPort); /* Server port */
D&C

## Slide 35: TCP Echo Client (cont)
/* Establish the connection to the echo server */
if (connect (sock, (struct sockaddr *) &echoServAddr, sizeof(echoServAddr)) < 0) DieWithError("connect() failed");
echoStringLen = strlen(echoString); /* Determine input length */
/* Send the string to the server */
if (send (sock, echoString, echoStringLen, 0) != echoStringLen)
DieWithError("send() sent a different number of bytes than expected");
/* Receive the same string back from the server */
totalBytesRcvd = 0; /* Count of total bytes received */
printf("Received: "); /* Setup to print the echoed string */
D&C

## Slide 36: TCP Echo Client (cont)
while (totalBytesRcvd < echoStringLen)
{
/* Receive up to the buffer size (minus 1 to leave space for
a null terminator) bytes from the sender */
if ((bytesRcvd = recv (sock, echoBuffer, RCVBUFSIZE - 1, 0)) <= 0) DieWithError("recv() failed or connection closed prematurely");
totalBytesRcvd += bytesRcvd; /* Keep tally of total bytes */
echoBuffer[bytesRcvd] = '\0'; /* Terminate the string! */
printf("%s", echoBuffer); /* Print the echo buffer */
}
printf("\n"); /* Print a final linefeed */
close (sock);
exit(0);
}
D&C

## Slide 37: TCP Sockets Summary
Sockets Address Structure
TCP and UDP Call Sequences
Socket
Connect
Bind
Listen
Accept
Close
TCP Echo Server and Client [old]

## Slide 38: TCP Socket Calls
socket()
bind()
listen()
read()
close()
socket()
connect()
read()
write()
close()
blocks until server receives
a connect request from client
data
data
Server
Client
accept()
write()
connect negotiation

## Slide 39: UDP Socket Calls
socket()
bind()
sendto()
close()
socket()
bind()
recvfrom()
sendto()
close()
blocks until server
receives data from client
data
data
Server
Client
recvfrom()
Not needed