## Slide 1: Project 1
In essence:
Use libpcap to examine packet captures
Parse packet headers in software to understand the packets
Create lists of data based on what was in the packet captures

## Slide 2: Welcome to The Datalink Layer!

## Slide 3: Key Concepts
Framing
  Sentinel, Counter-Based, Clock-Based
Medium Access
  Ethernet, Wireless, Token Ring
Switching and Forwarding
  Datagrams, Source Routing, Spanning Tree
Switch Design
  Shared bus/memory, Crossbar, Self-routing
Error Detection
  CRC, Parity, Checksum

## Slide 4: Framing
Breaking bits into manageable units called frame
Implemented by network adaptor
Main approaches
  Sentinel-based
  Counter-based
  Clock-based

## Slide 5: Sentinel-based Framing
Delineate frames with a special pattern (e.g., 01111110)‏
Ethernet
Problem: special pattern is in the payload
Solution: Bit stuffing
  Sender: insert 0 after 5 consecutive 1s
  Receiver: delete 0 that follows 5 consecutive 1s
Commonly used in the Ethernet

## Slide 6: Counter-based Framing
Include a payload length field in the header
Problem: count field corrupted
Solution: corruption caught by CRC calculation
This example is from a protocol called Digital Data Communication Message (DDCM)
Commonly used in TCP and IP header

## Slide 7: Medium Access
Ethernet (bus)
Wireless (802.11)
Token Ring (FDDI)

## Slide 8: Ethernet
Developed by Xerox PARC mid 1970s
Similar to IEEE 802.3 standard
CSMA/CD
  Carrier Sense
  Multiple Access
  Collision Detection
Frame Format
Notes: CS: able to listen to see if anyone else is transmitting at the same time.
MA: multiple ppl are trying to communicate over the bus at the same time. It will guarantee that they can transmit at the same time but help with error recovery
CD:

## Slide 9: Ethernet
Addresses
  unique, 48 bit addresses assigned to each NIC
  Example: 08:00:E4:B1:02:01 6 bytes
  Broadcast: all 1s
  Multicast: first bit is 1
Bandwidth: 10Mbps, 100Mbps, 1Gbps
Length: 2500m (500m segments with 4 repeaters)
Problem: fair distributed resource management
Notes: Repeaters simply broadcasted info to all the other three repeaters. To go over 500m, we needed to use a repeater.
2500 is just length of ethernet segment. It doesn’t mean that Ethernet only supports 2500 length
If multiple stations transmit at the same time, so long the length is under 2500, it can detect collision.
Now ethernets use switches. Can have 2500m upto a switch.

## Slide 10: Transmit Algorithm
If line is idle
  Send immediately
  Upper bound of 1500 bytes
  Must wait 9.6 microsecs between frames
If line is busy
  Wait until idle, transmit immediately

## Slide 11: Collisions
Source A
Source B
Receiver
Communication
Channel
Unintelligible
Protocol
Violation

## Slide 12: Collisions
If there is a collision...
  Send JAM for 32 bits, then stop transmitting
  (Continue sending from a collision so the other will stop)
  Minimum frame: 64 bytes (header, plus 46 data)
  Delay and try again:
    1st time: 0 or 51.2 microseconds
    2nd time: 0, 51.2, or 102.4 microseconds
    nth time: k * 51.2 microsecs, random k = 0...2n-1
    Give up after a lot of tries (usually 16)
    Exponential back-off
      Doubling the amount of wait time
Notes: Continue sending from a collision so the other will stop

## Slide 13: Ethernet
Ethernet is lousy at fairness and collisions
Why do we still use it?
  Cheap
  Easy to administer
  Multiple access is actually less common
    Ethernet hub/repeater are not popular anymore; instead, Ethernet switches are seen more commonly

## Slide 14: Ethernet Networks
Bus topology, multiple hosts connected to each other
Repeater devices attach segments together
  "Hubs" commonly used for this (see notes)
Is this what is used in Ethernet networks today?
  NO. Switch based topologies using these old hubs
Notes: A repeater with more than two ports was commonly called a hub; hubs allowed branching and thus much more complex topologies.
It was the rise of hubs that enabled star topologies in which each host connects directly to the hub rather than to one long run of coax. This in turn enabled twisted-pair cable: while this supported maximum runs of about 100 meters, versus the 500 meters of thick coax, each run simply had to go from the host to the central hub in the wiring closet
While repeaters act at the bit layer, a switch reads in and forwards an entire packet as a unit, and the destination address is consulted to determine to where the packet is forwarded. Except for possible collision-related performance issues, hubs and switches are interchangeable. Eventually, most wiring-closet hubs were replaced with switches.

## Slide 15: Wireless
Can use radio or infrared
  Infrared diffused, but only about 10m
11Mbps, 54Mbps
  With 5G (current), you are transmitting faster than that
Avoiding interference (Spread Spectrum)
  Frequency hopping
  Direct sequence (chipping code)
Medium Access
  Same thing as Ethernet?
  Answer on the next slide

## Slide 16: Ad-hoc Wireless
Multiple Access Collision Avoidance (MACA)
  Request to Send (RTS)
  Recipient sends Clear to Send (CTS)
What do you do if
  You see a CTS and RTS, someone is communicating with you so you should listen
  you see a CTS, but you're not the sender?
  you see an RTS, but no corresponding CTS?
    The other party is not authorized to send
    Or you are not able to hear other party replying (out-of-range)
Other features
  ACK signal
  Mangled RTS messages?

## Slide 17: Wireless with Access Points
Handshaking process:
  Mobile device sends Probe
  Base station replies with Probe Response
  Mobile device sends Association Request
  Base station sends Association Response
Active scanning
  During an active scan, the client radio transmits a probe request and listens for a probe response from an AP.
Beacons
  short, regular transmissions from access points that inform user devices about available Wi-Fi services and nearby access points.

## Slide 18: Token Ring
IBM Token Ring (802.5)
Ring of computers
Data travels either clockwise or counter-clockwise, but not both
  Not a series of point links
Token allows possessor to speak on the ring
  Sent data collected by speaker
  Round-robin, limited quantum

## Slide 19: Token Ring (2)
Node failure breaks the ring?
  Electromechanical Relay can fix it
Multi-station access unit (MSAU)
  Dynamic relays, makes it look like a star topology
Access control?
  Token: 24 bits
  Seize the token, send preamble
  Token Holding Time: 10ms
  Reservation bits in frame header
  Early release vs. delayed release
Confirmed delivery (A bit, C bit)

## Slide 20: Token Ring Monitors
Distributed Election
  Candidates run (claim token), highest address wins
Monitor must:
  Add delay when needed
  Ensuring a token exists
    Timer used to notice missing token
  Reaping checksum errors and orphans
    Monitor bit
  Detecting subtle breaks with beacons

## Slide 21: FDDI (optic fiber) vs. Token Ring
Changes due to fiber instead of copper
  Relays not the same
  Dual ring structure
  4B/5B encoding vs. differential Manchester
  Uses control signals instead of illegal encoding

## Slide 22: Packet Switching

## Slide 23: Switching and Forwarding
Large networks can be constructed with switches
Can connect hosts/switches via point-to-point links
Adding hosts to a switch may not decrease performance for other hosts

## Slide 24: Datagram Switching
Destination | Port
A | 3
B | 0
C | 3
D | 3
E | 2
F | 1
G | 0
H | 0

## Slide 25: Datagram Switching (2)
Connectionless / Immediate service
  Think of looking at one envelope at a time and forwarding it to its destination
Host never knows if the network can handle the traffic
Packets traverse independently
  Even if they are part of the same message
Failures may not bring the network down

## Slide 26: Source Routing
Source provides full switching information in header of packet
Header size?
  Become very large
Large networks?
  Not great for large n/ws

## Slide 27: Implementation and Performance
Commodity machines with several network cards
Direct memory access, CPU header inspection
I/O and memory bandwidth limiting component
  Packets copied twice
Small packets require more header lookups
Specially designed switches avoid this contention with hardware

## Slide 28: Switch Design
Input/Output Ports, Switching Fabric (n/w topology)
  Fabric has big impact on the performance
Fabric very simple: takes packet from input port to output port
  Self-routing fabrics do the heavy lifting themselves
FIFO queue can lead to head-of-line blocking
  Traffic bottlenecks like in Worcester
  Pure output buffering

## Slide 29: Switching Fabric
Shared Bus
Shared Memory
  High speed memory, avoids I/O bus
Crossbar
  Every input has direct channel to every output
Self-routing
  Hierarchy of cross-bar switches

## Slide 30: Crossbar Switching

## Slide 31: Self-Routing Fabric

## Slide 32: Circuit Switching
Seeking out and establishing a physical copper path from end-to-end [historic definition] .
Circuit switching implies the need to first set up a dedicated, end-to-end path for the connection before the information transfer takes place.
Once the connection is made, the only delay is propagation time.

## Slide 33: Circuit Switching
Figure 2-38. (a) Circuit switching. (b) Packet switching.
Tanenbaum

## Slide 34: Network Core: Circuit Switching
End-end resources reserved for “call”
link capacity, router buffer space
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 35: Connection-Oriented Virtual Circuits
Figure 5-45.Internetworking using concatenated
virtual circuits.
Tanenbaum

## Slide 36: Store-and-Forward Networks
Intermediate processors (IMPS, nodes, routers, gateways, switches) along the path store the incoming block of data.
Each block is received in its entirety at the router, inspected for errors, and retransmitted along the path to the destination.
This implies buffering at the router and one transmission time per hop.

## Slide 37: Message Switching
A store-and-forward network where the block of transfer is a complete message.
Since messages can be quite large, this can cause:
  buffering problems at the router.
  high mean delay times.

## Slide 38: Packet Switching
A store-and-forward network where the block of transfer is a complete packet.
A packet is a variable length block of data with a fixed upper bound.
**Using packets improves mean message delay.

## Slide 39: Packet Switched Networks
Connection-Oriented Protocols
A setup stage is used to determine the end-to-end path before a connection is established.
Data flow streams are identified by some type of connection indicator (e.g. OSI, X.25, SNA, ATM).

## Slide 40: Packet Switched Networks
Connectionless Protocols
No set up is needed.
Each packet contains information which allows the packet to be individually routed hop-by-hop through the network.
Split and adaptive routing techniques are possible.

## Slide 41: Connectionless Internetworking
Figure 5-46. A connectionless internet.
Tanenbaum

## Slide 42: Datagram vs Virtual Circuit
Datagram Routing
  Each datagram packet may be individually routed.
Virtual Circuit Routing
  In virtual circuit, set up is required.
  All packets in a virtual circuit follow the same path through the network.

## Slide 43: Transmission Event Timing
DCC 6th Ed., W. Stallings, Figure 10.3

## Slide 44
Virtual Circuit and
Datagram Operation
DCC 6th Ed.,
W. Stallings,
Figure 10.4

## Slide 45
Virtual Circuit and Datagram Operation
DCC 6th Ed.,
W. Stallings,
Figure 10.5

## Slide 46: Networking Switching Summary
Circuit-switching and message switching are now obsolete.
Store-and- forward, datagram packet switching (IP routers) dominates the Internet.
Cell switching and virtual circuits (ATM switches) still exists in ATM networks.
The external protocol abstraction to the subnet may differ from the internal subnet view.
  e.g., TCP is a connection-oriented protocol that runs on top of a datagram IP protocol.